## Slide 1: AI Chips - A Brief Introduction

## Slide 2: Overview
1. Brief Introduction
2. Top Players and Their Chip Architecture
  Graphcore IPU
  Tenstorrent
  Cerebras WSE
  Google TPU
  Huawei 910/310
  Alibaba Hanguang800
3. Leverage the advantage of CIM
  Competitor -- Mythic

## Slide 3: Brief Introduction
Scalar
CPU
Vector
CPU + AVX512
GPU
What is next??
What is next??

## Slide 4: Brief Introduction
Scalar
CPU
Vector
CPU + AVX512
GPU
Graph
Graphcore IPU
Tenstorrent GraySkull
Cerebras WSE
Neural network is DAG (Directed Acyclic Graph).

## Slide 5: Brief Introduction
Scalar
CPU
Vector
CPU + AVX512
GPU
Matrix/Tensor
Google TPU (systolic array)
Huawei Ascend 910/310 (CUBE)
Alibaba Hanguang800 (Tensor Engine)
Nvidia GPU + TensorCore
Matrix multiple dominates neural network calculations.

## Slide 6: Top Players and Their Chip Architecture

## Slide 7: Top Players – Graphcore IPU
IPU is built for graph and designed for intelligence.
Simon Knowles, CTO Graphcore

## Slide 8: Top Players – Graphcore IPU
Compute
1216 IPU-tiles (small cores)
Special MAC unit
Memory
300MB on-chip SRAM
256KB local SRAM per tile
45TB/s memory bandwidth
37GB/s memory BW per tile
No external DRAM
Communication
8TB/s no-blocking all-to-all exchange

## Slide 9: Top Players – Graphcore IPU
IPU is built for graph （Computation is a graph）.
https://www.youtube.com/watch?v=k_jR7DfN67c

## Slide 10: Top Players – Graphcore IPU
Takeaways
  Graph processor
  Computation: Multicore architecture
  Memory: Near memory computation (300MB distributed on-chip SRAM and no external DRAM)
  Interconnect / Network: 8TB/s no-blocking all-to-all exchange

## Slide 11: Top Players – Tenstorrent GraySkull
“GPU was built for running programs on pixels not executing graphs. Tenstorrent builds processor to run graph natively.” -- Jim Keller
Jim Keller is the first investor of Tenstorrent and he is the CTO of this company now.
https://www.youtube.com/watch?v=G4hL5Om4IJ4

## Slide 12: Top Players – Tenstorrent GraySkull
“Tenstorrent builds processor to run graph natively.” -- Jim Keller

## Slide 13: Top Players – Tenstorrent GraySkull
Compute
120 cores
Vector, SIMD
Memory
>120MB on-chip SRAM
1MB local SRAM per core
84TB/s memory bandwidth
~700 GB/s memory BW per core
External DRAM
Communication
330GB/s NoC bandwidth

## Slide 14: Top Players – Tenstorrent GraySkull
Takeaways
  Graph processor
  Computation: Multicore architecture
  Memory: >120MB on-chip SRAM and external DRAM
  Interconnect / Network: 330GB/s NoC bandwidth

## Slide 15: Top Players – Cerebras WSE

## Slide 16: Top Players – Cerebras WSE

## Slide 17: Top Players – Cerebras WSE

## Slide 18: Top Players – Cerebras WSE
2D mesh NoC

## Slide 19: Top Players – Cerebras WSE

## Slide 20: Top Players – Cerebras WSE
Takeaways
  Wafer Scale Engine
  Wafer Scale Engine
  Wafer Scale Engine

## Slide 21: Top Players – Google TPU
DDR3
  Store models (kernels / weights)
Matrix Multiply Unit
  MAC
Accumulators
  Accumulation
Activation Pipeline
  BN, ResAdd, sigmoid, Relu…
Activation Storage
  Store feature map

## Slide 22: Top Players – Google TPU
DDR3 ->（DDR4?）
  Store models (kernels / weights)
Matrix Multiply Unit -> (CIM)
  MAC
Accumulators -> (Psum Adder)
  Accumulation
Activation Pipeline -> (SFU)
  BN, ResAdd, sigmoid, Relu…
Activation Storage -> (8MB SRAM)
  Store feature map

## Slide 23: Top Players – Google TPU
CONV data & computation flow
  (1) Load weight ->
  (2) MAC ->
  (3) Accumulator ->
  (4) BN, ResAdd, sigmoid, relu… ->
  (5) Store feature map
2
1
3
4
5

## Slide 24: Top Players – Google TPU
Changes from TPUv1 to TPUV2
  Single vector memory instead of buffers
  General purpose vector unit instead of a fixed activation pipeline
  Connect matrix unit as an offload for the vector unit
  Move to HBM for bandwidth
  Add interconnect for scaling

## Slide 25: Top Players – Google TPU
Takeaways
  For simplicity, accumulator + activation pipeline (BN, ResAdd, Relu…) is good choice.
  For generality, vector unit + vector memory is a good choice.

## Slide 26: Leverage the advantage of CIM/PIM

## Slide 27: Leverage the advantage of CIM/PIM
The advantage of CIM/PIM:
  Never pay the energy of reading the weights
  Only pay the energy of performing the MAC ops
Mythic – Good Design Reference
  CIM /PIM
  Matrix Multiplying Memory (never read weights)
  SIMD unit
  RISC-V
  120 Tiles
  NoC interconnect
  No DRAM

## Slide 28: Leverage the advantage of CIM
What?
  CIM
    – Eliminate the need of weights movement
    – High computation density
Who / Who’ll buy?
  Data center
Why / Why they buy?
  Power efficiency

## Slide 29: Questions?

## Slide 30: Thank you!

## Slide 31: Backup

## Slide 32: Top Players – Huawei Da Vinci
CUBE
    8190 INT8 MACs
MTE
    Memory Transfer Engine
    Explicit memory hierarchy design
Vector Unit
    2048bit vector
Special functions:
  NMS
  ROI
  SORT

## Slide 33: Top Players – Huawei Da Vinci
Multi-thread hardware
The First layer is executed on vector unit
Balance computation power between CUBE vs Vector by overlapping its computation time with Vector
Carefully allocated the number of MACs in CUBE and Vectors

## Slide 34: Top Players – Cerebras WSE

## Slide 36: Roadmap of Tenstorrent’s processor